Fast Plane Extraction
- Plane segmentation algorithm for RGB-R images
- Takes advantage of the “image” organization
- Octree segmentation

---
Tangential Vectors
- Approximate neighbor with range image
- Tangential vectors using difference of neighbors

---
Normal Vector
The normal vector is computed using the cross product of two tangential vectors

---
Noise filtering
- Separate vectors into “component images”
- Apply Gaussian filter to images to smooth normals
  cv::GaussianBlur(*hori, *hori, cv::Size(3,3), 0);
  cv::GaussianBlur(*vert, *vert, cv::Size(3,3), 0);

---
Plane clustering
- Feed octree with the normal vectors as points.
- All normals in one voxel initially represents on plane

---
pcl::octree and trick
Good:
  - Fit out problem, we used a pcl::PointXYZNormal to encode the normal in XYZ and the point in the Normal to get it back after the computation
    pcl::PointXYZNormal.xyz = Norm
    pcl::PointXYZNormal.Norm = xyz
Bad:
  - Little and outdated documentation
  - C++ implementation using template of a template of an other template

---
Fast plane extraction First result
Plane have been split into two different voxels

---
Merge Similar Planes
- Compute mean of each plane
- Merge similar planes
- Nested “for” through all planes

---
Merge Result

---
Parallel plane distinction
- Same octree technique
- In this case the location is going to be given by the distance of each point to the plane defined by the common Normal vector.
    pcl::PointXYZNormal.x = pointToPlaneDist()
    pcl::PointXYZ.y = 0
    pcl::PointXYZ.z = 0
    pcl::PointXYZNormal.Norm = xyz

---
Final Result

---
Object Representation
- An object is represented by its parts:
  - A table is represented by four legs (cylinders) connected to a surface (plane)
- Distance between clusters is computed leading to a graph where vertices are types (cylinder, plane, etc...) and edges are “connections” (closeness between clouds)

---
Object location in Graph
Plane
Cylinder
Table model

---
Graph Algorithm
- Search is computed with a recursive algorithm
- For every vertex in the graph it is recursively compared to the every vertex in the object graph
- Compare every vertex neighbor to every object vertex neighbor